## Slide 1
08 – Introduction to Remote Sensing
Chair of Sensor-based Geoinformatics (geosense)
www.geosense.uni-freiburg.de
Passive vs. active remote sensing
Common data types
Remote Sensing Platforms

## Slide 2: Difference active & passive remote sensing?
08 – Introduction to Remote Sensing

## Slide 3: Passive vs. active remote sensing
Passive remote sensing
Reflected energy of another light source (e.g. sun) is recorded
Typical instrument: Camera, Linescanner
Active remote sensing
Energy is emitted (actively) and recorded
Typical instrument: Light Detection and Ranging (LiDAR), Radio and Ranging (RADAR)
Sketch Tablet
https://ursaspace.com/wp-content/uploads/2021/09/Remote20Sensing-03.jpg
https://ursaspace.com/wp-content/uploads/2021/09/Remote20Sensing-02.jpg

## Slide 4: Passive vs. active remote sensing
Passive remote sensing
+ Easy to understand & acquire
+ Easy to interpet
- Dependency on sun (quantity/quality)
- Cannot penetrate objects (only 2D)
Active remote sensing
+ 3D or structural information
+ can be operated almost at any time
- Complex to operate and analyse
- Often expensive
Sketch Tablet
https://ursaspace.com/wp-content/uploads/2021/09/Remote20Sensing-03.jpg
https://ursaspace.com/wp-content/uploads/2021/09/Remote20Sensing-02.jpg

## Slide 5: Common data types
08 – Introduction to Remote Sensing

## Slide 6: Rasters
Typical Sensors: Cameras, Linescanners
Ideal for continuous mapping in space and time
Structured as matrices
  Easy to analyse (world as a grid)
  Sometimes problematic (nature is no grid)

## Slide 10: Point Clouds
Typical Sensors: LiDAR
Good for 3D representation
Unstructered data
  More challenging for analysis
  Allows more accurate representation

## Slide 13: What sensor platforms exist?
08 – Introduction to Remote Sensing

## Slide 14: Sensor platforms
Spaceborne
Satellites, Space station
Airborne
Drones, Airplanes, Balloons
Terrestrial & close range
Smartphones, terrestrial LiDAR Camera traps, …
Coverage
Spatial detail

## Slide 15: Sensor platforms
Drone (DJI Mavic 3E)
Commercial Copter
Pixel size: 0.03 m
Airplane
National Flight Surveys
Pixel size: 0.30 m
Spaceborne, Sentinel-2
ESA
Pixel size: 10 m
Coverage
Pixel size

## Slide 16
The importance of spatial resolution at the example of detecting dead trees.
Mosig et al. 2024

## Slide 17: Sensor platforms
Terrestrial LiDAR (TLS)
Commercial system (Riegl)
ca. 2000 points / m³
Drone LiDAR (ULS, UAV-LiDAR)
Commercial system (Riegl)
ca. 500 points / m³
Airborne LiDAR (ALS)
National Aerial Survey Germany
ca. 80 points / m³
Coverage
Pixel size

## Slide 18: To see, or not to see, that is the question
LiDAR is a powerful technqiue for 3D sensing but it also has limits!
Gassiloud et al. 2024

## Slide 20
+

## Slide 21: Best sensor & platform for forest inventories?
08 – Introduction to Remote Sensing